## Slide 1: Measuring for Growth Monitoring
Adapted from training materials of the Royal College of Paediatrics and Child Health [RCPCH]

## Slide 2: Measuring Weight
Babies should be weighed without any clothes or nappy
Children older than two years can be weighed in vest and pants, but no shoes, footwear, and dolls or teddies in hand
Only grade 3 clinical electronic scales in metric setting should be used -green sticker with background letter M (which means approved for medical use). Scales should be calibrated and maintained annually.

## Slide 3: Measuring Head Circumference
Measurement should be taken at the maximum occipito-frontal circumference taking the largest of 3 consecutive measurements
Head circumference should be measured using a narrow non- stretchable plastic or disposable lasso tape. Clean tape with antiseptic wipes [or soapy water] between child use

## Slide 4: Measuring Length
Measure length before age 2 years if concerned.
Use proper equipment (length board or mat) as any other method is too inaccurate. Requires one measurer and one other adult e.g. parent.
Length should be measured without nappy or footwear.

## Slide 5: Measuring Height
Height should be measured from ages 2 years using a rigid rule with T piece, or stadiometer.
Ensure heels, bottom, back and head are touching the apparatus with eyes and ears at 90°.
Don’t try to stretch up, measure on expiration.
Take three successive measurements and use the largest of the three.
Always measure with shoes removed

## Slide 6: Summary: Measuring
Whoever measures a child should be suitably trained or be supervised by someone who is
Weight
  Use only class lll electronic scales. Calibrated and maintained annually.
  Weigh babies naked, toddlers in vest and pants, without shoes
Head circumference
  Use narrow, paper or plastic non stretchable tape round widest part of the head
Length (up to approx age 2)
  Proper equipment essential (length board or mat)
  Training particularly important
  Shoes and nappy removed
Height (after age 2 or when child can weight bear independantly)
  Rigid rule with T piece, or stadiometer, shoes removed
Take three successive measurements and use the largest of the three